## Slide 1: CSEE 4823 F18 Project Binary-Weight, Binary Activation Neural Network Accelerator based on Latch-based Weight Memory
Dewei Wang, Shixin Qin, Paul Huang
dw2773, sq2210, xh2373

## Slide 2: Goal and Architecture
Goal: Architecture simplicity
Architecture: +1/-1 weights; +1/-1 activations; 784-1024-1024-1024-10 fully-connected; two-way MAC; latch-based weight memory; 1R1W weight memory;
Any reference?
Mem
2x4
Reg
ALU
G
Control
Re
g

## Slide 3: Characterization Methods and Results
Methods
  Input: 20-k test dataset from the MNIST benchmark
  RTL coding from a scratch: Yes
  Throughput: PT with DC-gen. sdf annotation
  Maximum clock frequency: PT with DC-gen. sdf annotation
  Energy efficiency: PT with the DC-gen. sdf and QS-gen. vcd annotations
  Area and number of gates: DC-gen report
  Accuracy: using the 20-k test dataset from the MNIST benchmark
Results
  Throughput: 1 [Mclassficiation/s]
  Maximum clock frequency: 40 [MHz]
  Energy efficiency: 1.3 [µJ/classification]
  Area and number of gates: 0.232 [mm2] and 123,456 gates
  Total memory bits: 256 [kB]
  Accuracy: 98.32%

## Slide 4: Copy your RTL (not netlist) and the testbench in a single file; double-click below↓
Copy your run.do file; double-click below↓