## Slide 1: CSEE 4823 F18 Project Binary-Weight, Binary Activation Neural Network Accelerator based on Latch-based Weight Memory
Dewei Wang, Shixin Qin, Paul Huang
dw2773, sq2210, xh2373

## Slide 2: Goal and Architecture
Goal: Accuracy and energy-efficiency
Architecture: +1/-1 weights; +1/-1 activations; 784-1024-1024-1024-10 fully-connected; latch-based weight memory; 1R1W weight memory; FSM control

## Slide 3: Characterization Methods and Results
Methods
  Input: 20-k test dataset from the MNIST benchmark
  RTL coding from a scratch: Yes
  Throughput: Tested in RTL simulation
  Maximum clock frequency: The minimum clock period in timing.tcl to meet the slack in PT and DC-gen report file.
  Area and number of gates: DC-gen report (memory has not been synthesized)
  Accuracy: using the 20-k test dataset from the MNIST benchmark
Results
  Throughput: 12 [classficiation/s]
  Maximum clock frequency: 200 [MHz]
  Area and number of gates: 0.004304 [mm2] and 393 gates memory has not been synthesized)
  Total memory bits: 4[MB]
  Accuracy: 97%

## Slide 4: Copy your RTL (not netlist) and the testbench in a single file; double-click below↓
Copy your run.do file; double-click below↓